## Slide 1: Presentation of Sliver Level Validation Points Metal detection robot Alpha Team Nov 13th2021

## Slide 2: Design specifications/Requirements
Contract : Create a robot that can search, detect and pick up all metallic objects in a given area
Bronze(DONE) :
  The robot is able to autonomously explore the area and detect metal objects.
  The robot is able to home in on the target.
Silver(Processing) :
  The robot is able to pick up the object and get back to his starting point.
  The robot is able to choose between multiple search path depending on the situation.
Gold :
  The robot is able to discriminate the picked-up objects by checking their color and prioritize targets.
Platinum :
  The robot is able to report to a remote system, with a graphical user interface.

## Slide 3: Project Plan
Requirement Validation
Design Test phase
Functional regression testing
Parallel Test cases execution (unit testing)
Peer reviews
Deployment
Design Firmware requirement
Design Firmware & Software development
Development Firmware
Peer reviews
Design Hardware architecture
Development Hardware
Project Plan
Iterative Validation Phase

## Slide 4: Validation Plan
Verification: Testing the product whether it meets the requirement.
Validation: Validating requirement meets the target standard
V-Model: the development and QA activities are done simultaneously. the V model of testing was developed where for every phase, in the Development life cycle there is a corresponding Testing phase.

## Slide 5: Requirements Under test
R001 to R004 are for Bronze Level.
R005 - The robot chooses the most suitable path to approach the metallic object.
R006 - The robot stops when it detected the metallic object (verified in R004 last time).
R007 - Pick-up scenario with the Pick-up Module.
R008 - The robot moves outside the test area, then heads to the safe area to drop the metal object and finally returns to the starting point.

## Slide 6: Search Patterns for validation cases
eV3
Home Target
Muster Point
Creeping line
10cm
20cm
eV3
Parallel track
Expanding Square search track

## Slide 7: Validation case 1
eV3
Home Target
Muster Point
Total test box is 100cm each side
10cm
20cm
eV3
Non - Metal object into the area

## Slide 8: Validation case 2
eV3
Home Target
Muster Point
Total test box is 100cm each side
10cm
20cm
eV3
Metal object into the area

## Slide 9: Validation case 3
eV3
Home Target
Muster Point
Total test box is 100cm each side
10cm
20cm
eV3
Non metal & Metal objects into the area

## Slide 10: Validation case 1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.

## Slide 11: Validation Tests
Validation case 1: Non-metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points:
Check Entry point Sensor1(left wheel motor) and Sensor2(right wheel motor) works conditionally with identical configuration for 5cm straight, turn right 30 ° and straight 50 cm to complete the area of one line pattern.
Each straight line has 50 cm length and turns has 10 cm.
Place the plastic ball (3cm radius) into the area.
Here IR sensor (S1) has to detect the object in less than 1cm range.
Check Inductive proximity sensor (S2) must be inactive as this object is not metal.
Once S1 = On, S2 = off, then robot has to stop and take the decision of “diversion”.
Here diversion condition has to work with the multiple turns with slow speed.
Total test box is 100cm each side
Non - Metal object into the area
eV3
eV3
eV3

## Slide 12: Validation Tests
Validation case 1: Non-metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement right side)
-check Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed and angle change 90°and move for 3cm
Stop at 3cm distance, take another turn of 90°(Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed ) and move ahead with slow speed until it achieves 10cm (original area of one side distance)
Total test box is 100cm each side
5cm
10cm
10cm
10cm
10cm
10cm
5cm
55 cm
60 cm
50 cm
eV3
eV3

## Slide 13: Validation Tests
Validation case 1: Non-metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement left side)
-Place any other object at right side.
-Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed and angle change 90°and move for 3cm
-Here if IR sensor (S1) = still On, then it has to take 180 °angle change and takes other path.
Check Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and rotation change of 180 °and stops.
Ensure robot moves for 6cm straight
eV3
Object which make robot to take other direction (different path)
Total test box is 100cm each side
5cm
10cm
10cm
10cm
10cm
10cm
5cm
55 cm
50 cm
eV3

## Slide 14: Validation Tests
Validation case 1: Non-metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement left side)
-Stop at 6cm distance, take another turn of 90°(Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and move ahead with slow speed until it achieves 20cm (original area of one side distance)
Object which make robot to take other direction (different path)
eV3
5cm
10cm
10cm
10cm
10cm
10cm
5cm
55 cm
50 cm
eV3

## Slide 15: Validation Tests
Validation case 1: Non-metallic object detection scenario with IR sensor
Autonomous area
100cm each side
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points:
Then, verify another Sensor1(left wheel motor) and Sensor2(right wheel motor) has to start working on the previous condition (identical speed)
Movement straight should achieve 50cm, but at 58th cm of travel, robot should stop.
Then here, condition of rotation should check that,
Sensor2(right wheel motor) = 0, Sensor1(left wheel motor) = speed 30, angle of rotation 30° , travel length 20cm (2*times of wheel rotation) for the turns.
-after the final turn, robot should travel 100cm for the exit to home target.
Total test box is 100cm each side
Non - Metal object into the area

## Slide 16: Validation case 2: Ensure robot has identified the metallic object and takes decision to pick and return to the exit and towards safe zone to drop the object. Here condition we have implemented is “Break the rules” which robot should break the condition of autonomous area exploration once it identified metal object.

## Slide 17: Validation Tests
Validation case 2: Metallic object detection scenario with IR sensor
Case2: Ensure robot has identified the metallic object and takes decision to pick and return to the exit and towards safe zone to drop the object. Here condition we have implemented is “Break the rules” which robot should break the condition of autonomous area exploration once it identified metal object.
Verification points:
Check Entry point Sensor1(left wheel motor) and Sensor2(right wheel motor) works conditionally with identical configuration for 5cm straight, turn right 30 ° and straight 50 cm to complete the area of one line pattern.
Place the object in the pattern area. Either turn or straight line,
Here IR sensor (S1) has to detect the object in less than 1cm range.
Check Inductive proximity sensor (S2) must be active as this object is metal.
Once S1 = On, S2 = On, then robot has to stop and slow the speed until it touch the metal.
Total test box is 100cm each side
Metal object into the area
eV3
EV3 towards muster point with object

## Slide 18: Validation Tests
Validation case 2: Metallic object detection scenario with IR sensor
Verification points:
After that, Ev3 sensor (S3&S4) which is having the pick up arms, - It should act for 90 °as we have placed it in horizontal direction.
Pick up the metal and load it over the arms.
Then important point is : S2 and S1 should Off at this point to ensure metal object is taken by robot arm.
Break the autonomous area condition, and with respective algorithm, robot should move to the exit (by subtracting the remaining total area value)
And place the object in the safe zone by the sensor 3 and sensor 4 (Arm)
Reverse degree of rotation value should work to place the object in the safe place.
then S1&S2 should = On until we turns to 180 °returns to the home target.
Total test box is 100cm each side
eV3
Home Target
Muster Point
10cm
20cm
eV3

## Slide 19: Validation case 3: Ensure robot has identified the non-metallic object and takes decision to diversion, then identified the metal object and break the autonomous area condition and start working towards the pick up and drop object condition.

## Slide 20: Validation Tests
Validation case 3: Non metallic and metallic object detection scenario with IR sensor
Case3: Ensure robot has identified the non-metallic object and takes decision to diversion, then identified the metal object and break the autonomous area condition and start working towards the pick up and drop object condition.
Verification points:
Check Entry point Sensor1(left wheel motor) and Sensor2(right wheel motor) works conditionally with identical configuration for 5cm straight, turn right 30 ° and straight 50 cm to complete the area of one line pattern.
Place the object in the pattern area. Either turn or straight line,
Here IR sensor (S1) has to detect the object in less than 1cm range.
Check Inductive proximity sensor (S2) must be active as this object is metal.
Once S1 = On, S2 = On, then robot has to stop and slow the speed until it touch the metal.
Total test box is 100cm each side
5cm
10cm
10cm
10cm
10cm
10cm
5cm
55 cm
50 cm

## Slide 21: Validation Tests
Validation case 3: Non metallic and metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement right side)
-check Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed and angle change 90°and move for 3cm
Stop at 3cm distance, take another turn of 90°(Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed ) and move ahead with slow speed until it achieves 10cm (original area of one side distance)
Total test box is 100cm each side
5cm
10cm
10cm
10cm
10cm
10cm
5cm
55 cm
60 cm
50 cm
eV3
eV3

## Slide 22: Validation Tests
Validation case 3: Non metallic and metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement left side)
-Place any other object at right side.
-Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed and angle change 90°and move for 3cm
-Here if IR sensor (S1) = still On, then it has to take 180 °angle change and takes other path.
Check Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and rotation change of 180 °and stops.
Ensure robot moves for straight towards to defined pattern area.
Object which make robot to take other direction (different path)
eV3
Total test box is 100cm each side
5cm
10cm
10cm
10cm
10cm
10cm
5cm
55 cm
50 cm
eV3

## Slide 23: Validation Tests
Validation case 3: Non metallic and metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement left side)
-Place any other object at right side.
-Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed and angle change 90°and move for 3cm
-Here if IR sensor (S1) = still On, then it has to take 180 °angle change and takes other path.
Check Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and rotation change of 180 °and stops.
Ensure robot moves for straight towards to defined pattern area.
Total test box is 100cm each side
5cm
10cm
10cm
10cm
10cm
10cm
5cm
55 cm
50 cm

## Slide 24: Validation Tests
Validation case 3: Non metallic and metallic object detection scenario with IR sensor
Verification points:
After that, Ev3 sensor (S3&S4) which is having the pick up arms, - It should act for 90 °as we have placed it in horizontal direction.
Pick up the metal and load it over the arms.
Then important point is : S2 and S1 should Off at this point to ensure metal object is taken by robot arm.
Break the autonomous area condition, and with respective algorithm, robot should move to the exit (by subtracting the remaining total area value)
And place the object in the safe zone by the sensor 3 and sensor 4 (Arm)
Reverse degree of rotation value should work to place the object in the safe place.
then S1&S2 should = On until we turns to 180 °returns to the home target.
eV3
Home Target
Muster Point
10cm
20cm
eV3
Total test box is 100cm each side
5cm
10cm
10cm
10cm
10cm
10cm
5cm
55 cm