## Slide 1: Presentation of Bronze Level Validation Points Metal detection robot Alpha Team Oct 17th2020

## Slide 2: Design specifications/Requirements
Contract : Create a robot that can search, detect and pick up all metallic objects in a given area
Bronze :
  The robot is able to autonomously explore the area and detect metal objects
  The robot is able to home in on the target
Silver :
  The robot is able to pick up the object and get back to his starting point
  He is able to choose between multiple search path depending on the situation
Gold :
  The robot is able to discriminate the picked up objects by checking their color, and prioritize targets
Platinum :
  The robot is able to report to a remote system, with a graphical user interface.

## Slide 3: Project Plan
Requirement Validation
Design Test phase
Functional regression testing
Parallel Test cases execution (unit testing)
Peer reviews
Deployment
Design Firmware requirement
Design Firmware & Software development
Development Firmware
Peer reviews
Design Hardware architecture
Development Hardware
Project Plan
Iterative Validation Phase

## Slide 4: Validation Plan
Verification: Testing the product whether it meets the requirement.
Validation: Validating requirement meets the target standard
V-Model: the development and QA activities are done simultaneously. the V model of testing was developed where for every phase, in the Development life cycle there is a corresponding Testing phase.

## Slide 5: Requirements Under test
R001 - Performance of EV3 boot up with OS and Program able to exécutable.
R002 - The robot find the area autonomously (Defined 60cm square travel).
R003 - Non-metallic object detection scenario with IR sensor.
R004 - Metallic object detection scenario with IR and Inductive proximity sensor.
R005 - The robot pick up the metallic object and carry till drop location.
R006 - The robot drops metal out of area (in another location but not the starting point).
R007 - The robot returns to starting point.
Bronze level

## Slide 6: Requirements on Spot
eV3
eV3
eV3
eV3
Autonomous area
Metal object
Non Metallic object
Home Target
Muster Point
Entry
Exit
60cm each side
10cm
20cm
Different path selection

## Slide 7: Validation Tests
Verification of R001: Performance of EV3 boot up with OS and Program able to exécutable
No. | Test cases | Expected results | Actual results
1 | Check the batteries. | Four batteries should be installed and be charged. | 
2 | Check the SD card. | SD card should be installed and have appropriate OS files. | 
3 | Press the main button to activate. | EV3 should start booting and load OS files | 
4 | Ensure the LED colors are appropriate | Make sure it takes <2 min’s to boot up with the following LED colors. Orange and Green if it was successfully installed | 
5 | Check the firmware file executability. | Confirm programming file extension with “*” format. If not program cannot be executed. | 

## Slide 8: Validation Tests
Verification of R002: The robot find the area autonomously (Defined 60cm length each side).
No. | Test cases | Expected results | Actual results
1 | Find and run the programmed file. | The file should be complied successfully and without error on GUI. | 
2 | Put the robot at home point and check it moves to the defined area. | The robot should start moving into the area in based on the algorithm defined. | 
3 | Ensure entry and exit point of the robot maintained while it travel in the defined area. | When robot moves straight, turns, each declared conditions must work without an error. | 

## Slide 9: Validation Tests
Verification of R002: The robot find the area autonomously (Defined 60cm square travel).
eV3
Autonomous area
Home Target
60cm each side
10cm
Case1: Verify robot able to move from home target to entry point
10cm straight
Verification points:
Verify the sensor 1(left wheel motor)and sensor 2 (right wheel motor) simultaneously to move forward with the same speed. condition (1)
Ensure normal speed is maintained and direction is straight.
Before the rotation (angle), confirm the Sensor1(left wheel motor) and right stops at same time,
And sensor 1(left wheel motor) set = 0, and On sensor 2 (right wheel motor) = 20cm (overall both the outer diameter of wheel distance), condition (2)
20cm angle change
Once the speed it achieved, check condition (3) should activate and make sure for both the wheels till the entry point.
eV3
eV3

## Slide 10: Validation Tests
Verification of R002: The robot find the area autonomously (Defined 60cm square travel).
eV3
Autonomous area
Home Target
60cm each side
10cm
Case2: Ensure the conditions are working by following calculations,
Key variables:
Total travel distance
360°degree angle measurement
Speed of the motor rotates the wheel
On and Off sensors based on the conditions achieved.
Sample equation:
To find distance travel :
= Total length of travel (Each side area) / One rotation of the wheel x 360°
Note: Utilizing Threads or Move tank mechanism to keep both the motor On and Off at same time.

## Slide 11: Validation Tests
Verification of R002: The robot find the area autonomously (Defined 60cm square travel).
eV3
Autonomous area
60cm each side
Case3: Ensure robot moves smoothly in the defined area with defined algorithm.
Verification points:
Verify robot able to identify entry and stops (sleep(2000)).
From entry point, sensor 1(left wheel motor)and sensor 2 (right wheel motor) should act as identical (speed) for only straight( forward)
Movement straight should achieve 60cm, but at 58th cm of travel, robot should stop.
Then here, condition of rotation should execute that,
sensor 2 (right wheel motor) = 0, sensor 1(left wheel motor) = speed 30, angle of rotation 90° , travel length 20cm (2*times of wheel rotation)
-Once the above condition has achieved, robot should stop for a while (sleep(1000))

## Slide 12: Validation Tests
Verification of R002: The robot find the area autonomously (Defined 60cm square travel).
eV3
Autonomous area
60cm each side
Case3: Ensure robot moves smoothly in the defined area with defined algorithm.
Verification points:
Then, ensure another sensor 1(left wheel motor)and sensor 2 (right wheel motor) has to start working on the previous condition (identical speed)
Movement straight should achieve 60cm, but at 58th cm of travel, robot should stop.
Then here, condition of rotation should check that,
sensor 2 (right wheel motor) = 0, sensor 1(left wheel motor) = speed 30, angle of rotation 90° , travel length 20cm (2*times of wheel rotation)
-once the above condition has achieved, robot should stop for a while (sleep(1000))

## Slide 13: Validation Tests
Verification of R002: The robot find the area autonomously (Defined 60cm square travel).
eV3
Autonomous area
60cm each side
Case3: Ensure robot moves smoothly in the defined area with defined algorithm.
Verification points:
Then, ensure another sensor 1(left wheel motor)and sensor 2 (right wheel motor) has to start working on the previous condition (identical speed)
Movement straight should achieve 60cm, but at 58th cm of travel, robot should stop.
Then here, condition of rotation should check that,
sensor 2 (right wheel motor) = 0, sensor 1(left wheel motor) = speed 30, angle of rotation 90° , travel length 20cm (2*times of wheel rotation)
-once the above condition has achieved, robot should stop for a while (sleep(1000))

## Slide 14: Validation Tests
Verification of R002: The robot find the area autonomously (Defined 60cm square travel).
eV3
Autonomous area
60cm each side
Case3: Ensure robot moves smoothly in the defined area with defined algorithm.
Verification points:
Then, verify another Sensor1(left wheel motor) and Sensor2(right wheel motor) has to start working on the previous condition (identical speed)
Movement straight should achieve 60cm, but at 58th cm of travel, robot should stop.
Then here, condition of rotation should check that,
Sensor2(right wheel motor) = 0, Sensor1(left wheel motor) = speed 30, angle of rotation 90° , travel length 20cm (2*times of wheel rotation)
-once the above condition has achieved, robot should stop for a while (sleep(1000))

## Slide 15: Validation Tests
Verification of R002: The robot find the area autonomously (Defined 60cm square travel).
eV3
Autonomous area
Home Target
60cm each side
10cm
Case3: Ensure robot reached the exit point and able to move back to home target.
Verification points:
From exit point, validate sensor left = 0 Sensor2(right wheel motor) = speed 20, angle of rotation 90° , travel length 18cm (1*times of wheel rotation)
After the rotation, ensure condition of identical speed is Sensor1(left wheel motor) and right has working towards 10 cm
It has to stop at the home point

## Slide 16: Validation Tests
Verification of R003: Non-metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points:
Check Entry point Sensor1(left wheel motor) and Sensor2(right wheel motor) works conditionally with identical configuration for 30cm,
Place the plastic ball (3cm radius)
Here IR sensor (S1) has to detect the object in less than 1cm range.
Check Inductive proximity sensor (S2) must be inactive as this object is not metal.
Once S1 = On, S2 = off, then robot has to stop and take the decision of “diversion”.
Here diversion condition has to work with the multiple turns with slow speed.
eV3
Non Metallic object
eV3

## Slide 17: Validation Tests
Verification of R003: Non-metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement right side)
-check Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed and angle change 90°and move for 3cm
Stop at 3cm distance, take another turn of 90°(Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed ) and move ahead with slow speed until it achieves 20cm (original area of one side distance)
eV3
Non Metallic object
60cm total length one side
30cm
10cm
20cm

## Slide 18: Validation Tests
Verification of R003: Non-metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement left side)
-Place any other object at right side.
-Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed and angle change 90°and move for 3cm
-Here if IR sensor (S1) = still On, then it has to take 180 °angle change and takes other path.
Check Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and rotation change of 180 °and stops.
Ensure robot moves for 6cm straight
eV3
eV3
60cm total length one side
30cm
10cm
20cm
Object which make robot to take other direction (different path)

## Slide 19: Validation Tests
Verification of R003: Non-metallic object detection scenario with IR sensor
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points: (robot movement left side)
-Stop at 6cm distance, take another turn of 90°(Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor2(right wheel motor) should set as = 0, Sensor1(left wheel motor) set slow speed ) and move 3cm straight.
Stop at 3cm distance, take another turn of 90° (Sensor1(left wheel motor) should set as = 0, Sensor2(right wheel motor) set slow speed ) and move ahead with slow speed until it achieves 20cm (original area of one side distance)
eV3
eV3
60cm total length one side
30cm
10cm
20cm
Object which make robot to take other direction (different path)

## Slide 20: Validation Tests
Verification of R003: Non-metallic object detection scenario with IR sensor
eV3
Autonomous area
60cm each side
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points:
Then, verify another Sensor1(left wheel motor) and Sensor2(right wheel motor) has to start working on the previous condition (identical speed)
Movement straight should achieve 60cm, but at 58th cm of travel, robot should stop.
Then here, condition of rotation should check that,
Sensor2(right wheel motor) = 0, Sensor1(left wheel motor) = speed 30, angle of rotation 90° , travel length 20cm (2*times of wheel rotation)
-once the above condition has achieved, robot should stop for a while (sleep(1000))

## Slide 21: Validation Tests
Verification of R003: Non-metallic object detection scenario with IR sensor
eV3
Autonomous area
60cm each side
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points:
Then, verify another Sensor1(left wheel motor) and Sensor2(right wheel motor) has to start working on the previous condition (identical speed)
Movement straight should achieve 60cm, but at 58th cm of travel, robot should stop.
Then here, condition of rotation should check that,
Sensor2(right wheel motor) = 0, Sensor1(left wheel motor) = speed 30, angle of rotation 90° , travel length 20cm (2*times of wheel rotation)
-once the above condition has achieved, robot should stop for a while (sleep(1000))

## Slide 22: Validation Tests
Verification of R003: Non-metallic object detection scenario with IR sensor
eV3
Autonomous area
60cm each side
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points:
Then, check another Sensor1(left wheel motor) and Sensor2(right wheel motor) has to start working on the previous condition (identical speed)
Movement straight should achieve 60cm, but at 58th cm of travel, robot should stop.
Then here, condition of rotation should check that,
Sensor2(right wheel motor) = 0, Sensor1(left wheel motor) = speed 30, angle of rotation 90° , travel length 20cm (2*times of wheel rotation)
-once the above condition has achieved, robot should stop for a while (sleep(1000))

## Slide 23: Validation Tests
Verification of R003: Non-metallic object detection scenario with IR sensor
eV3
Autonomous area
Home Target
60cm each side
10cm
Case1: Ensure robot has identified the non metallic object and takes decision to move ahead for searching the metallic object into the defined area.
Verification points:
From exit point, sensor left = 0 Sensor2(right wheel motor) = speed 20, angle of rotation 90° , travel length 18cm (1*times of wheel rotation)
After the rotation, ensure condition of identical speed is Sensor1(left wheel motor) and right has working towards 10 cm
It has to stop at the home point

## Slide 24: Validation Tests
Verification of R004: Metallic object detection scenario with Inductive proximity sensor
Case1: Ensure robot has identified the metallic object and takes decision to pick and drop the object in the safe area (which is not home point)
Verification points:
Entry point Sensor1(left wheel motor) and Sensor2(right wheel motor) works conditionally with identical configuration for 30cm,
Place the aluminum cans(5cm radius)
Here IR sensor (S1) has to detect the object in less than 1cm range.
Check Inductive proximity sensor (S2) must be active as this object is metal state.
Once S1 = On, S2 = On, then robot has to stop and take the decision of “Pick up the object”.
eV3
Metallic object

## Slide 25: Validation Tests
Verification of R004: Metallic object detection scenario with Inductive proximity sensor
Case1: Ensure robot has identified the metallic object and takes decision to pick and drop the object in the safe area (which is not home point)
Verification points:
When IR sensor = active, then Sensor1(left wheel motor) and right should stop near to the object.
Here Inductive proximity sensor also should set as = active,
When this condition has achieved, then sensor 1 and sensor 2 should set as “0”.
Sensor 3 and sensor 4 should act as a arm, working at same speed to pick the object and lodge into the space.
After pickup the material, IR sensor and Inductive proximity sensor should set automatically = 0, when this condition has achieved then sensor 1 (left wheel motor) set as =0, and sensor 2 (right wheel motor) set as slow speed and change the angle of robot 180° (U-turn).
eV3
Metallic object

## Slide 26: Validation Tests
Verification of R004: Metallic object detection scenario with Inductive proximity sensor
Case1: Ensure robot has identified the metallic object and takes decision to pick and drop the object in the safe area (which is not home point)
Verification points:
-Travel 30cm towards entry point and stop the sensor 1 and 2.
Sensor 1 must set as off, sensor 2 set as slow speed with angle of rotation 90°
Verify Travel straight to 20cm to reach muster point(safe place)
Drop the object with the help of sensor 3 and 4.
Again sensor 1 (left wheel motor) set as =0, and sensor 2 (right wheel motor) set as slow speed and change the angle of robot 180° (U-turn).
Travel straight 30cm to reach and stopped.
eV3
Metallic object
Home Target
Muster Point
10cm
20cm

## Slide 27: Thank you